## Slide 1: Megawatts and Gigawatts on the way to Terawatts
Kathy Ayers, Proton OnSite

## Slide 2: Problem Definition
Need ~10 TW of carbon free energy by 2050
  Most renewables are intermittent
  Energy storage at this scale is required
To address the terawatt problem, we have to install megawatts and gigawatts first
  Leverage technologies at this scale now even if they “can’t” get to terawatts in the long term
  Innovation often happens in well understood technology

## Slide 3: Why we shouldn’t (just) wait for new/better/more ideal technology
Storage needed now
Growing global energy needs
Increasing renewables
New Technologies:
Lab validation to market penetration is >20 years
All technologies have challenges, we just haven’t found them all yet
% Renewable electricity in mix
by geographic region, 2010 to 2050

## Slide 4: Technology Development Timeline: Getting to 2050
Stolten, October 2014: “The Potential Role of Hydrogen Technology for Future Mobility. How Can this Improve Our Life?”
(CO2 emissions)

## Slide 5: How can we make an earlier impact?
Implement higher TRL tech
  New technology is 10-12 years from any impact
Problem is here today: wind
  160 GW in Germany and China alone, stranding 20-40%
  270 GW expected by 2020
Even installing MW systems today takes time to get to GW
Shift at least 10 years for new technology
Global installed wind ~400 GW

## Slide 6: How Real is the 20 year Product Cycle?
Tesla Production History
Toyota produces >10,000,000 vehicles/year
Tesla: an “agile and innovative” example
Founded in 2003
  Existing, well established battery chemistry
  Cars are not a totally new invention
  Minimal sales till 2013
Even good ideas struggle
  Almost went bankrupt in 2008
Gigafactory expected to be running in 2017
  18650 Li-ion battery has been sold since 1991

## Slide 7: Why does development take so long?
Not just about materials/performance
Manufacturing is its own science
  Cost and uniformity at scale
Durability testing takes time
Interactions can derail a system
  Impact of tolerance extremes
Design for safety and code compliance adds complexity
Electrode Structure
Efficiency
Durability
Processability
Catalyst system example

## Slide 8: The Risks of Shortcutting Development
Boeing 787 Dreamliner battery packs
Laptop at Japan conference
Navy stress test for submarine energy system

## Slide 9: Case Study: Importance of Renewable Hydrogen
Global demand >600 billion Nm3/yr – Largely driven by NH3
Flexibility as an energy storage medium
Page 9

## Slide 10: Impact
$118 billion in market revenues projected
2% of US energy currently goes through H2 more than 95% by natural gas reforming
If 2050 US H2 projections can be produced from renewables, it could cut
45% of all US carbon emissions
2500 M metric tons of CO2
Slide courtesy of Bryan Pivovar, NREL 2016

## Slide 11: Proton’s Experience: Timeline and Product Cost Evolution
Product Type | S-Series | H-Series | C-Series | Megawatt
Year Introduced | 2000 | 2004 | 2012 | 2015
Units Sold | 450+ | 200+ | 22+ | NA
H2 output (Nm3/hr) | 1 | 6 | 30 | 200–400
Generates | 1 Day | 1 Day | 1 Week | 1 Day
Replaces | Six Pack | Tube Trailer | Jumbo Tube Trailer | Jumbo Tube Trailers
Starting from a well-established technology in 1996
Input Power
6 kW
36 kW
180 kW
1 - 2 MW
$/kW vs. S-Series
100%
43%
28%
13%

## Slide 12: Figures of Merit for MW scale electrolysis
Water usage: 1000 gal/day/MW
Total electrode area: 27 m2/MW (~50 m2 of membrane)
Cell current: ~1260 A
Catalyst cost: $50K/MW ($50/kW)
Hydrogen produced: 400 kg/day/MW
Cars fueled: ~70/day (depending on storage)
Comparison to Solar Fuels TRL:
Typical goal metric: 100 cm2 electrode at 10 mA/cm2
Equivalent to less than 1 gram of H2/day

## Slide 13: Is there enough platinum (and iridium)?
Power per annual production (Rossmeisl, 2014):
Pt Fuel cells: ~0.3 TW
Ir Electrolysis: ~0.1 TW
Need ~ 1-2 order of magnitude increase in activity to be relevant for global energy storage needs
Pathways:
3M NSTF
Core shell catalysts
Spray deposition

## Slide 14: Necessity can force innovation
Emissions control well beyond what was known to be possible
*Courtesy of Ellen Stechel, ASU

## Slide 15: MW Status
+500,000 cell hours accumulated to date on stack design
Idle to Full Load
in less than 10 sec

## Slide 16: Opportunities and Challenges

## Slide 17: The US Agency H2 Gap
Electrolysis Needs
NASA
AMO
ARPA-E
DoD
OE
EERE
ManTech
High pressure, separations
Energy storage, non-H2
High risk, high reward
$/kg focus; overall portfolio
Cross-industry manufacturing
H2 applications limited

## Slide 18: Need to Leverage Synergies
What PEC can do for electrolysis
Materials development
  Ion exchange membranes (low H2 permeation)
  OER catalysts
  Non-PGM catalyst supports
Manufacturing
  Large scale catalyst synthesis
  Electrode fabrication methods
What electrolysis can do for PEC
Balance of plant for water-gas management
Controls and safety circuit development
Validation of large scale H2 production
Integration experience

## Slide 19: Conclusions
Need to be realistic about the timeframes for technology development
Government funding challenges to be addressed
Address near term needs as well as new science and discovery
Find synergies between both and drive progress