## Slide 1: Simulated annealing for crystal structure determination
Materials Department
University of California, Santa Barbara
June 4th, 2014
Ryan Latture

## Slide 2: Given a composition what is the crystal structure?
Ga
As
Wavelength (nm)
Spectral Irradiance
Quantum Efficiency (%)
500
1500
3000
10
20
30
0.4
0.8
.12
.16
Hubbard, Seth, and Ryne Raffaelle. "Boosting solar-cell efficiency with quantum-dot-based nanotechnology." SPIE Newsroom (2010).
Notes: Arbitrary composition -> get crystal structure -> predict properties
Spectral Irradiance W m-2 nm-1

## Slide 3: Outline
Introduction to simulated annealing
  SA algorithm
  Benchmarking key aspects
Application to crystal structure:
  Global minimum of Lennard-Jones clusters
  Simulated annealing aided with x-ray diffraction
  Automated assembly of secondary building units

## Slide 4: Overview of simulated annealing
Global minimization technique:
  Suitable for objective functions with many local minima.
Named for the annealing process in metals.
  Begin at high “temperature”
  Cooling schedule determines end state

## Slide 5: Steps in simulated annealing algorithm
Start: define cost function & initial guess
Generate randomized candidate solution
Yes
No
Is candidate better than current solution?
Replace current solution with candidate solution
Replace current solution with given probability:
Reached maximum number of iterations?
No
Stop
Yes
Decrease temperature

## Slide 6: Visualizing simulated annealing
Optimum Solution
Start
Randomized
Jump

## Slide 7: Benchmarking key aspects of simulated annealing
Step Size
  Dictates the amount of the landscape that is probed
Temperature
  Cooling too quickly possible convergence on local optimum

## Slide 8: Choose step size based on specific landscape
Start: (2.5,2.5)
Iterations: 100,000
Temperature:
T is constant
Step size:
0.01

## Slide 9: Appropriate step size speeds up convergence
Start: (2.5,2.5)
Iterations: 8,000
Temperature:
T is constant
Step size:
1.0

## Slide 10: Logarithmic temperature quickly converges to a solution
Start: (2.5,2.5)
Iterations: 2,000
Temperature:
T decreases logarithmically
Step size:
1.0
Notes: Initial temperature:
generate N random points around initial guess
Evaluate cost for each candidate
Store max and min cost values
Compute
If , return T
Else, /
N=n+1
p=2
Initial temperature:
generate N random points around initial guess
Evaulate cost for each candidate
Store max and min cost values
Compute 𝜒(𝑇_𝑛 )=(𝑠𝑢𝑚 exp⁡〖𝐸𝑚𝑎𝑥 〗)/(𝑠𝑢𝑚 exp⁡𝐸𝑚𝑖𝑛 )
If 𝜒(𝑇_𝑛 )−𝜒_𝑜<𝑡𝑜𝑙𝑒𝑟𝑎𝑛𝑐𝑒, return T
Else, 𝑇_(𝑛+1)=𝑇_𝑛 (𝑙𝑛𝜒(𝑇_𝑛 )/𝜒(𝑇_𝑛 ))^(1/𝑝)
N=n+1
p=2
𝑇_1=−∑▒((〖𝐸_𝑚𝑥−𝐸〗_𝑚𝑛))/(‖𝑆‖ln⁡(𝜒_𝑜))
𝑇_1

## Slide 11: Linear temperature is slower but more successful
Start: (2.5,2.5)
Iterations: 8,000
Temperature:
T decreases linearly
Step size:
1.0

## Slide 12: Summary of simulated annealing
Step size distance between local minima
Initial temperature between local minima
Cannot know the optimum choice a priori
  Adaptive SA algorithm

## Slide 13: Outline
Introduction to simulated annealing
  SA algorithm
  Benchmarking key aspects
Application to crystal structure:
  Global minimum of Lennard-Jones clusters
  Simulated annealing aided with x-ray diffraction
  Automated assembly of secondary building units

## Slide 14: SA applied to 13 atom Lennard-Jones cluster
Initial guess
Global minimum
Lennard-Jones Potential:

## Slide 15: SA used to study structural transitions
309-atom L-J cluster
Noya, Eva G., and Jonathan PK Doye. "Structural transitions in the 309-atom magic number Lennard-Jones cluster." The Journal of chemical physics 124.10 (2006): 104503.
Notes: Desc LJ -> desc cluster -> SA technique ->
It is well established that, for N<1000, LJ clusters follow an icosahedral pattern growth, showing magic numbers corresponding to complete Mackay icosahedra at N=13, 55, 147, 309, 561, and 923. In between these magic numbers, the vast majority of the global minima correspond to a Mackay icosahedron core covered with an incomplete outer layer.
A Mackay icosahedron can be considered to be made up of 20 slightly distorted fcc tetrahedra sharing a common vertex
~107-108 MC cycles with 32 systems at different temperatures
All the temperatures were initialized with the Mackay icosahedron ground-state structure.
Evaporation and fragmentation of the cluster were avoided by adding a hard wall of radius r+sigma
v is the mean vibrational freq. For LJ potential reflects number of nearest neighbors and average neighbor distance. The latter because the second derivative of the LJ potential decreases with distance. Strained structures, which inevitably have a variety of nearest-neighbor distances, have a larger average nearest-neighbor distance, because of the anharmonic nature of the LJ well, and hence have smaller values of v
2^1/6*sigma = eq. separation distance
Epsilon = pair well depth
all the atoms in the interior of these clusters have 12 nearest neighbors, whose local coordination shell can be characterized as icosahedral, decahedral, fcc, or hcp.
The isomers found in zone 2A are Mackay icosahedra in which a pit is formed on one side of the cluster, while an adatom island is formed on the opposite side
Zone 2B: aggregates of fcc tetrahedra with six atoms per edge (instead of 5)
Zone 3, is occupied by isomers with a 147-atom Mackay icosahedral core, but where the outer layer has undergone a surface reconstruction from a Mackay to an antiMackay overlayer. Results in 279 atom structure with 30 atoms left over.
Zone 4, is associated with completely melted structures, in which both the core and surface atoms are disordered.

## Slide 16: Solving for crystal structure using diffraction data
Coelho, A. A. "Whole-profile structure solution from powder diffraction data using simulated annealing." Journal of applied crystallography 33.3 (2000): 899-908.
Objective function:
AlVO4
Notes: Echem comprises empirical information about equilibrium covalent bonding geometry, vibrations, and hydrogen-bonded and non-bonded
interactions in accordance with prior knowledge of these quantities obtained from small molecule crystallography and spectroscopy.
Eexp describes the difference between observed and computed diffraction data.
Aluminum Orthovanadate

## Slide 17: SBUs reduce degrees of freedom
Mellot-Draznieks, Caroline, Stéphanie Girard, and Gérard Férey. "Novel inorganic frameworks constructed from double-four-ring (D4R) units." Journal of the American Chemical Society 124.51 (2002): 15326-15335.
D4R building unit
Theoretical structures
Notes: Echem comprises empirical information about equilibrium covalent bonding geometry, vibrations, and hydrogen-bonded and non-bonded
interactions in accordance with prior knowledge of these quantities obtained from small molecule crystallography and spectroscopy.
Eexp describes the difference between observed and computed diffraction data.

## Slide 18: Conclusions
Simulations using Lennard-Jones potentials can model systems with large number of atoms.
Any information to about the crystal structure will speed up convergence.
  Diffraction data
  AASBU

## Slide 19: Questions?