## Slide 1: Recycling Nuclear Waste: Potentials and Global Perspectives
Mikael Nilsson
Department of Chemical Engineering and Materials Science
University of California, Irvine
TeraWatts, TeraGrams, TeraLiters
UC Santa Barbara, Monday Feb 2, 2015

## Slide 2: Current Nuclear Fuel Cycle
The current US approach is a once-through fuel cycle
  There is currently ~70,000 MT of used fuel in the US which should be disposed in a geologic repository.
The composition of the used fuel is ~96% uranium, ~1% TRU (mostly Pu) and ~3% fission products.
The used nuclear fuel must be managed, monitored, and isolated.

## Slide 4: What are the consequences? Are there better options?
http://www.ocrwm.doe.gov/info_library/newsroom/photos

## Slide 5: Identifying alternative options
In 2011, US-DOE initiated a study for Nuclear Fuel Cycle Evaluation and Screening.
    Different suggestions for nuclear fuel cycles suggestions were collected.
  Over 4000 different options for fuel cycles were found and compounded into 40 different groups.
    EG01-EG40 where EG01 is reference, current, nuclear fuel cycle.)
9 different evaluation criteria were developed
  6 related to benefits (resources, safety, waste etc), 3 related to challenges (financial, development, etc)
https://inlportal.inl.gov/portal/server.pt/community/nuclear_science_and_technology/337/online_nuclear_fuel_cycle_options_catalog
Nuclear Fuel Cycle Evaluation and Screening Final Report, US-DOE

## Slide 6: Study Summarized

## Slide 7: Conclusions
The fuel cycles providing the highest benefit are :
  Continuous recycle of U/Pu with new natural-U (Nat. U) fuel in fast critical reactors
  Continuous recycle of U/TRU with new Nat. U fuel in fast critical reactors
  Continuous recycle of U/TRU with Nat. U fuel in both fast and thermal critical reactors
  Continuous recycle of U/Pu with new Nat. U fuel in both fast & thermal critical reactors
Costs for development of these fuel cycles would range from $2B-$10B (for U/Pu) and $10B-$25B (for U/TRU) for development to engineering scale followed by $10B-$25B (for U/Pu) and $25B-$50B (for U/TRU) for development to commercial facility. Implementation of the industrial fleet is comparable to maintaining current reactor fleet.

## Slide 8: Levelized Cost at Equilibrium

## Slide 9: With already existing technology we can:
Reuse up to 97% of the material
Reduce the volume of waste considerably
Reduce the need for mining and enrichment
Increase the utilization of uranium by a factor of ~100.
We still face the challenge of handling a long lived waste product.

## Slide 10: Sellafield, UK 6 square km 10,000 employees 50+ years of reprocessing 50,000 tons of used fuel have been recycled to date

## Slide 12: International collaboration may be required
Countries that have nuclear power reactors might not have the option to invest in recycling facilities.
Countries that have already existing capabilities can receive the used fuel from other countries, remove the reusable material and prepare the waste form.
Requires transportation of used nuclear fuel across the world.

## Slide 13: MOX plant construction (Aqueous-polishing)
http://www.moxproject.com/construction/

## Slide 14: Can we transport waste safely?

## Slide 15: To Dream the Impossible Dream
What could we do to avoid:
  Storing radioactive material for an eternity?
  Using less than 1% of the useful resources?
Used Nuclear fuel contains potentially valuable material, Rh, rare earths, Pd.
  Can we recover and reuse some of these elements?

## Slide 18: Grand Challenges
Advanced separation processes.
Advanced materials
Nonproliferation and perceived safety.
Political decisions, or lack thereof.
Long term investments and security.

## Slide 19
H2 can be manufactured cleanly by using nuclear energy for water-splitting
Nuclear
Reactor
Low Temp.
Electrolysis
Thermo- chemical
High Temp.
Electrolysis
Heat
Electricity
H2
Courtesy of Ken Schultz

## Slide 20: Scheme for Nuclear assisted CO2 capture from Coal combustion

## Slide 21: The CO2 credit is a key parameter
A modest CO2 credit allows synfuel via nuclear H2 production to compete with coal synfuel
Coal gasification synfuel cost estimated from Rentech study (http://www.rentechinc.com/process-technical-publications.htm)

## Slide 22: Burning synfuel made from captured CO2 results in ZERO CO2 net release
Century Gothic 24 bold
Century Gothic 24 bold
Century Gothic 24 bold
CO2 produced during fuel manufacturing
CO2 released upon fuel combustion
Net CO2 released
Annual production of CO2 from manufacturing and combustion of synfuel from various sources

## Slide 23: Thank You